Instruction Types and Format

OPCODE : Operation Code
rs: Source Register
rt: Temporary Register
rd: Destination Register
shamt: Shift Amount (To be implemented in future update)

R-type Instruction:

I-type Instruction:

J-type Instruction:

We have chosen this instruction format so that each part of the instruction consists of 4 or multiple of 4 bits which makes it easier to convert into comprehensible HEXA codes.

        Instructions Set:
R-Type
Instruction	Name		Action		opcode		funct
ADD rd, rs, rt	Addition		rd = rs + rt		0000		0000
SUB rd, rs, rt	Subtraction		rd = rs – rt		0000		0001
AND rd, rs, rt	AND		rd = rs & rt		0000		0010
OR rd, rs, rt	OR		rd = rs | rt		0000		0011
NOR rd, rs, rt	NOR		rd = ~(rs | rt)		0000		0100
NAND rd, rs, rt	NAND		rd = ~(rs & rt)		0000		0101
I-Type
Instruction		Name		Action		opcode
SW rt, offset(rs)		Store Word		M[offset + rs] = rt		0001
LW rt, offset(rs)		Load Word		rt = M[offset + rs]		0010
BEQ rs, rt, offset		Branch On Equal		if(rs==rt) than pc = pc + offset		0011
J-Type
Instruction		Name		Action		opcode
J target		Jump		pc = target[0-11];		0100

ALU CONTROL:
ALU Control Lines	Function
0000	AND
0001	OR
0010	NOR
0011	NAND
0100	ADD
0101	XOR
1100	SUB

ALU Control Truth Table:

ALUOP1	ALUOP0	FUNCT FIELD				OPERATION
		F3	F2	F1	F0
0	0	X	X	X	X	0100
X	1	X	X	X	X	1100
1	X	0	0	0	0	0100
1	X	0	0	0	1	1100
1	X	0	0	1	0	0000
1	X	0	0	1	1	0001
1	X	0	1	0	0	0011
1	X	0	1	0	1	0010

Control Unit:

Instruction	Reg Dst	Op1	Op0	ALU / Src	Branch	MemRead	Mem Write	Reg Write	MemTo Reg	Jump
R- / Type	1	1	0	0	0	0	0	1	0	0
lw	0	0	0	1	0	1	0	1	1	0
sw	0	0	0	1	0	0	1	0	0	0
beq	0	0	1	0	1	0	0	0	0	0
bne	0	0	1	0	0	0	0	0	0	0
j	0	0	0	0	0	0	0	0	0	1

SAMPLE PROGRAM:
Add two numbers from memory:
1) lw $r1, 0[1]
2) lw $r2, 0[2]
3) add $r1, $r2, $r3
4) sw $r3, 0[3]

0001 0000 0001 0000 0000 0001	101001(Hex)
0001 0000 0010 0000 0000 0010	102002(Hex)
0000 0001 0010 0011 0000 0000	012300(Hex)
0010 0000 0011 0000 0000 0011	203003(Hex)

Datapath:

1 Bit Alu

24 bit ALU:

REGISTER FILE:

Control Unit

ALU Control: